## Slide 1: Transboundary cooperation for sustainable water management in the Sava River Basin
Dragan Zeljko
Deputy Secretary, ISRBC

## Slide 2: Sava River basin – basic facts
Country | Share of the basin (%) | Share of the territory (%)
Albania | 0.2 | 0.6
Bosnia & Herzegovina | 39.2 | 75.8
Croatia | 26.0 | 45.2
Montenegro | 7.1 | 49.6
Serbia | 15.5 | 17.4
Slovenia | 12.0 | 52.8
Main facts
  Area: ~ 97 700 km2 (2nd Danube sub-basin; share: 12%)
  Sava River length: 945 km
  Discharge: ~ 1700 m3/s (1st Danube tributary; contribution 25%)
  Active area of floodplains: 1700 km2

## Slide 3: Sava River basin - high environmental and socio-economic value
  High landscape and biological diversity
  Nature conservation : 176 sites; total area 17,231.24 km2

## Slide 4: Sava River basin - high environmental and socio-economic value
  Large retention areas - „living with floods”

## Slide 5: Legal framework for cooperation
Framework Agreement on the Sava River Basin – FASRB (the first development-oriented multilateral agreement in the region, 2004)
Parties: SI, HR, BA and RS
Key objective:
Transboundary cooperation
for sustainable development of the region
Specific goals:
  To establish an international regime of navigation
  To establish sustainable water management
  To prevent/limit hazards (floods, droughts, ice and accidents) and reduce/eliminate their negative consequences
Protocols to the FASRB:
  Regulate specific issues: navigation regime; emergency situations; sediment management; transboundary impacts; flood protection …
Implementing body: International Sava River Basin Commission

## Slide 6: Cooperation and Public participation
6
Stakeholders in the basin
  Governmental sector
  Non-governmental (civil) sector
  Academic sector (universities and institutes)
  Business sector (e.g. Coca-Cola)
Sava Water Council
  Advisory platform of ISRBC (NGO, academic, business sectors)
  55 institutions / organizations
Observers
  International organizations (ICPDR, DC)
  NGOs (WWF, Euronatur, etc.)
  GWP CEE, REC
  (FYR of) Macedonia, Montenegro
Youth Parliament
  Schools from the region

## Slide 7: Protocol on flood protection
7
Protocol regulates the issues of sustainable flood protection in the Sava River Basin with aim to prevent or limit flood hazard, to reduce flood risk and to reduce or mitigate detrimental consequences of floods.
Parties agreed to cooperate in:
  Development of the Sava Flood Risk Management Plan
  Development of the Sava Flood Forecasting, Warning and Alarm System
  Exchange of information
  Flood defence emergency situations and mutual assistance
  Other commonly agreed actions
Status : Signed in 2010; in force since Nov 2015.

## Slide 8: Flood Risk Management Plan
Initial steps
  Draft Program
  Initial flood vulnerab. assesment
  Joint PFRA Report (incl. May ‘14 flood)
Plan, incl. Summary of Measures (2017-2018)
Zagreb
Sisak
(Bosanski) Brod
Slavonski Brod
Sremska Mitrovica

## Slide 9: Data and information exchange
www.savagis.org
www.savahis.org
Principles (organizations, monitoring locations, data to be exchanged)
Routes (procedures, timetable, quality standards, use and redistribution, ownership, charging, future harmonization)
Organizations (HMSs, water agencies...)

## Slide 10
Flood forecasting and warning
NWP models
  ALADIN- short term (up to 3 days)
  ECMWF operational run/single forecast medium term (3-9 days)
  ECMWF EPS/ensembles
  WRF-NMM Serbia
  NMMB Serbia
  WRF-NMM Bosnia and Herzegovina
  Cosmo-EU Bosnia and Herzegovina
  WRF-NMM Montenegro
Hydrological models
  WFlow BA/RS/ME (to be developed through the project)
  HEC-HMS Sava basin
  Mike NAM Croatian sub-basin
  Mike NAM Una sub-basin
  HBV-light Bosna sub-basin
  HEC-HMS Kolubara sub-basin
  HBV Kolubara sub-basin
  HBV Jadar sub-basin
  Tamnava sub-basin
  Ub sub-basin
  Ljig sub-basin
Hydraulic models
  HEC-RAS Sava (from border Sl/HR-Danube)
  Mike 11 Croatian rivers
  HEC-RAS Una in BiH
  HEC-RAS Sana&Sanica
  HEC-RAS Vrbas
  Mike 11 Vrbas
  HEC-RAS Bosna
  HEC-RAS Usora
  HEC-RAS Drina
  HEC-HMS Kolubara
Hydrological forecasts and systems
  Results from Slovenian and Croatian operational systems
  EFAS, WMO SEE-FFGS
Real-time data collection system
  Sava HIS
SavaHIS components
Existing models
+
A distributed physically
based hydrological model
W-FLOW
DelftFEWS
Integration & Cooperation

## Slide 11: May 2014 flood – learning from disaster
11
11
11
Extreme event
  13-18 May heavy and continous rain over the basin

## Slide 12: May 2014 flood learning from disaster
12
12
12
Sanski Most (BA)
Doboj (BA)
Obrenovac (RS)
Flooded willage in Eastern Slavonia (HR)

## Slide 13: May 2014 flood – learning from disaster
13
13
13
Country | Affected | Evacuated | Casualties | Damage+losses (mil €) | Cause
Serbia | 1.6 million | 32 000 | 51 | Damage: 860 Losses: 662 Total: 1532 | Torrents, landslides, levee breach
Bosnia-Herzegovina | 1 million | 90 000 | 25 | 2 000 | Torrents, landslides, levee breach
Croatia | 38 000 | 15 000 | 3 | 297.6 | Levee breach
Termo Power Plant Nikola Tesla surrounded by flood waters, RS

## Slide 14: Lessons learnt from 2014 flood
Land Use and Spatial Planning
  Implement results of flood hazard and flood risk mapping in spatial plans of municipalities
  Municipalities should prohibit further development in real flood-prone areas and limit the increase of flood risk in potentially flooded areas through special conditions and permits
  Designate erosion-prone areas with a set of conditions for their use, to sustain existing forests, and afforest hilly and mountain regions in the Sava River Basin. These may prevent enormous sediment movement and landslides, which induced huge damages in May 2014
  Issue of environmental protection in case of flooding, since many hot-spots were endangered. Appropriate land use regulations and floodplain zoning needed
  Preserve existing retentions and natural floodplains, but also create new retention capacities, wherever possible. The use of existing reservoirs and retentions for flood management should be enhanced and coordinated between Sava countries

## Slide 15: Lessons learnt from 2014 flood
Non-structural measures
  Need for an efficient flood forecasting system
  Need for more efficient exchange of information before and during an event
  Need to model extreme scenarios, including dike breaches along the Sava River in various locations with the aim of evaluating the residual risk
  Improve meteorological and hydrological monitoring infrastructure as well as human capacities of responsible institutions.
  The needs of additional research on the mechanism of, warning on and response to torrential floods
  Special attention should be paid to rising of public awareness, and building the preparedness for quick reaction in case of torrential flood.

## Slide 16: Lessons learnt from 2014 flood
Preparedness and mitigation (rapid disaster response)
  Technical capacities of competent authorities have to be strenghtened
  Authorities on municipality level are not well prepared for handling such an extreme emergency situation, and the available plans have serious deficiencies. The update of these plans is needed and an appropriate training programme for municipalities and stakeholders has to be organized.
  Awareness of the communities on flood risk should be raised and maintained, with a clear understanding of their role in appropriate response to emergency situations
  Communication with media should be organized better.
  Emergency operations can be improved if both vertical and horizontal responsibilities are clearly defined
  Strenghten regional cooperation primarily through existing platforms ( i.e. ICPDR, ISRBC)

## Slide 17: Concluding remarks
Benefits of cooperation in a regional body:
  Good platform to discuss/solve regional/basin problems
  Exchange of information/experiences
  Possibility of development of integrated systems
  Can secure synergy between national and regional actions
  Harmonization of regulation, methodologies and procedures
  Brings together various stakeholders
Chalenges / possible obstacles:
  Differences among the countries in the process of EU accession and related obligations
  Financing of priority projects/strategic studies
    The enhancement of the fund-raising efforts possible through strengthening the ties and cooperation among, and with, the relevant national bodies
  Intersectoral cooperation in the countries

## Slide 18: Contact information
International Sava River Basin Commission
Kneza Branimira 29
10000 Zagreb
Croatia
www.savacommission.org